## Slide 1: A First Look at Commercial 5G Performance on Smartphones https://fivegophers.umn.edu/www20
Arvind Narayanan, Eman Ramadan, Jason Carpenter, Qingxu Liu, Yu Liu, Feng Qian, Zhi-Li Zhang
The Web Conference | Taipei 2020 | WWW 2020
Please don’t forget to install the fonts
provided besides this presentation.
After installing the fonts, please re-open this presentation.

## Slide 2: (Real) 5G Goes Live!
World’s first commercial 5G {services & smartphones} released in April 2019
  USA | Chicago & Minneapolis | Verizon | Moto Z3 + 5G Mod
  South Korea | Nationwide | SK Telecom | Samsung Galaxy S10 5G
Rapid surge in 5G deployments globally
[1] https://www.speedtest.net/ookla-5g-map
Total 5G City-Level Deployments 7372
Total 5G Operators 115
GLOBAL 5G STATISTICS [1]
Total 5G Smartphone Models 28
Notes: [click]
April 2019 marks the year when 5G commercial services and smartphones were finally rolled out.
This launch was witnessed by two cities in the United States and nation wide in South Korea.
[click]
Unlike 4G, 5G rollouts have been very rapid – not only in terms of deployments by carriers but also in terms of the number of smartphone model releases.
Globally speaking, within a year of 5G’s commercial launch, we have seen more than 100 carriers deploy their 5G services at several cites.

## Slide 3
Test
Enhanced Broadband
Throughput Capacity
Massive Connectivity
Large number of Connections
Mission Critical Communications
Low Latency & High Reliability
5G Promises To Overcome Several Limitations
1
2
3
100 Mbps reliably
>10 Gbps peak
1 million / km2
<1 ms latency
Smart City/IoT
V2X/AV
3D video, UHD streaming
AR/VR
CCTV
E-health
Notes: Rapid growth of 5G is not surprising because 5G promises to overcome several limitations posed by today’s existing 4G/LTE infrastructure.
Broadly speaking, [click] 5G promises to support 3 types of use-case scenarios.
[click]
Number 1: 5G enhances existing services by supporting very high data rates and traffic capacity. For example, 5G claims to support a peak traffic capacity of over 10 Gbps. Applications [click] such as 3D video and ultra-HD video streaming fall under this use case.
[click]
Number 2: 5G is expected to support enormous number of devices (such as low-cost sensors) that are applicable to [click] smart city deployments and industrial IoT.
[click]
Number 3: 5G is also designed to support mission critical applications that require extreme low latency and very high reliability [click] such as autonomous vehicles.
[click]
Of course there are many other applications that fall in between these scenarios such as virtual reality and e-health services among many others.
[click]
In this paper, we put these claims to test.
Before we get into it, let’s take a brief look at 5G technology.

## Slide 4: 5G Spectrum Bands
4G/LTE
5G
1 GHz
3 GHz
7 GHz
30 GHz
100 GHz
Low-Band
Mid-Band
High-Band
-NR (New-Radio)
Background (1/2)
Notes: A very critical aspect for any kind of [click] wireless communication is about frequency spectrums.
[click]
4G and the previous generations have gone up to 3 GHz of frequency range for communication.
[click]
However, 5G implies a very dramatic extension in the range of frequencies that it supports. 5G technology additionally extends all the way up to 100 GHz -- that is the millimeter wave range.
This is one of the key feature and characteristics of 5G causing a complete overhaul of the 5G radio all together.
Thus, the 5G radio is also referred to as [click] 5G-NR where NR stands for new radio.
5G’s wide frequency spectrum is divided into 3 categories [click] - low-band, mid-band and high-band.
While low-band and mid-band 5G subsumes all the previous generations of wireless technologies, high-band frequency range is rather new in the mainstream wireless communication ecosystem.
[click] Going to high frequencies are good in many ways, it opens up much more spectrums. This offers much higher bandwidth than 4G allowing for higher data transmission rates, but higher frequencies suffer from signal propagation issues making them very sensitive to obstructions.
Due to this physical layer issue, the coverage footprint provided of millimeter wave or high-band based 5G is comparatively very small.

## Slide 5: 5G Deployment Strategies
UE
5G-RAN
LTE-RAN
Non-Standalone (NSA)
LTE CORE
Data plane
Control plane
Background (2/2)
Supplement existing infrastructure investments
Control plane over LTE network
UE
5G-RAN
LTE-RAN
LTE CORE
5G CORE
UE
Standalone (SA)
No dependency on LTE
Fully exploit features provided by 5GC
Requires heavy infrastructure investments
Notes: We now take a look at how carriers can deploy 5G. Two deployment models have been standardized to meet initial market requirement.
[click]
The first one is called as “Non-Standalone 5G or NSA”.
In NSA, [click] the user equipment is able to simultaneously connect to both the LTE and 5G base stations.
[click] Such dual connectivity allows carriers to roll out 5G faster with minimal infrastructure investment.
[click] However, all the control plane signaling -- including that of 5G -- is now performed over LTE.
[click] The second deployment model is called the Standalone 5G or SA. In this model, at any given time, the user equipment can connect to either LTE or 5G base station.
[click] Thus there is no dependency of 5G on LTE.
[click] Standalone 5G will allow carriers to fully exploit 5G core architecture’s features such as network slicing, etc.
[click] This model however requires heavy investment.
[next]

## Slide 6: 5G Deployment Strategies
Background (2/2)
UE
5G-RAN
LTE-RAN
Non-Standalone (NSA)
LTE CORE
Data plane
Control plane
UE
5G-RAN
LTE-RAN
LTE CORE
5G CORE
UE
Standalone Mode (SA)
No dependency on LTE
Fully exploit features provided by 5GC
Requires heavy infrastructure investments
“Main drop”
All current 5G deployments follow this model
Supplement existing infrastructure investments
Control plane over LTE network
Notes: All current commercial 5G deployments worldwide follow the NSA model.
Next, let’s take a look at the commercial 5G landscape in the US.
[next]

## Slide 7: Commercial 5G for Smartphones in the US
Type | mmWave | mmWave | Mid-Band
Frequency | 28/39 GHz | 28/39 GHz | 2.5 GHz
Launch | April 2019 | June 2019 | May 2019
* As of October 2019, T-Mobile only offered mmWave-based 5G service. However, later in December 2019, they launched low-band 5G nationwide across the US.
All product and company names and/or logos are trademarks™ or registered® trademarks of their respective holders. Use of them does not imply any affiliation with or endorsement by them.
Motorola Z3 + Moto Mod 5G
Samsung Galaxy S10 5G
As of October 2019
Compatible with all carriers
Indoor
Deployment
Dense deployment of 5G Panels (mmWave)
Followed by many other models
5G-NR
Panel
5G-NR
Panel
(Facing back)
Close-up view of
5G-NR radio
Max Peak Speeds: 600 Mbps
Max Peak Speeds: 2 Gbps
Notes: As of October 2019, [click] three major carriers in the US had deployed their 5G services for consumers.
Interestingly, the carriers differed in their initial rollout strategies where Verizon and T-Mobile used millimeter wave, while Sprint used mid-band frequency.
[click]
The very first commodity 5G phones included Motorola’s Z3 and Samsung Galaxy S10 5G. The Z3 version required an additional accessory to access 5G network. US variants of both these phones used [click] Qualcomm’s X50 as 5G modem which supported Non Standalone 5G only. Subsequently many other phones were introduced as well.
[click]
Millimeter-based 5G Carriers such as Verizon had densely deployed 5G panels or base stations in their service areas which were often seen to be mounted over light poles. Each such site was equipped with one or more panels that acted as millimeter wave transceivers.
[click] For our experiments, we select Samsung’s S10 for two reasons.
[click] One, under similar experimental settings, S10’s throughput performance consistently outperformed Z3 by 2 to 3 times. [click] Secondly, S10 was the only smartphone compatible with the 5G service offered by all the three carriers.
[click] Hence, we select S10 to avoid any device-side artifacts that could possibly affect our experimental results.
While evaluating the 5G performance, [next] we faced several challenges.

## Slide 8
Challenges in Evaluating
5G Performance
Notes: we faced several challenges.
[next]

## Slide 9: Challenge 1: What to Study in Evaluating 5G Performance?
Physical-Layer Characteristics
Transport-Layer Factors
App. Behavior & Requirements
Carrier Infrastructure
UE-Side Factors
Server-Side Factors
The breadth of the 5G ecosystem makes it non-trivial to determine what to study
Challenges (1/4)
Our approach
Adopt a user-centric approach by strategically selecting measurement scenarios that highly impact end-users’ experience
Pay particular attention to implications of using mmWave
We also vary server-side factors such as server location and content delivery networks
Notes: Number 1 - There are many factors affecting 5G performance.
[click]
Right from physical layer characteristics such as the frequency spectrum used to Transport layer factors such as TCP configurations to meeting application requirements and behavior.
[click]
Equally important were factors such as the backhaul capacity of the carrier, user side factors such as user mobility or server-side factors such as server location.
[click]
Hence, the breadth of the 5G ecosystem made it non-trivial to determine what to study!
[click]
- To address this challenge, we adopt a user-centric approach by strategically selecting measurement scenarios that highly impact end users’ experience
[click]
- We also pay close attention to the implications of using millimeter wave which is considered key to mainstream 5G.
[click]
- We also vary server-side factors such as server location and content delivery networks.

## Slide 10: Challenge 2: No 5G Tool
US models (equipped with Snapdraggon 855 chipset) have locked bootloaders, no root access.
5G phones equipped with Android 9 Pie did not yet support 5G-NR APIs
5G
Challenges (2/4)
Notes: Coming to the next challenge.
[click]
US variants of 5G phones had locked bootloaders making it impossible for us to get root user privileges on the device.
[click]
The then state-of-the-art Android operating system version 9 did not yet support any 5G-NR APIs.
[click]
Thus, even when we were
connected to 5G [next] Running Android API

## Slide 11: Challenge 2: No 5G Tool
US models (equipped with Snapdraggon 855 chipset) have locked bootloaders, no root access.
5G phones equipped with Android 9 Pie which does not provide 5G-NR APIs
5G
getDataNetworkType() = ‘LTE’
Challenges (2/4)
How to detect if 5G is active?
How to detect handoff events?
No mature tool for capturing and monitoring 5G-specific information
Notes: calls such as getDataNetworkType() would return LTE even when connected to 5G.
[click]
Thus, our second challenge was that -- with no mature tool for accessing 5G related information, [click] questions such as how to detect 5G radio is active or how to detect handoff events remained unanswered.

## Slide 12: Challenge 2: No 5G Tool – Starting from Scratch
Challenges (2/4)
UE’s fine-grained location
Tower ID (cell ID) that the device is connected to
Cellular Signal Strength
5G-NR service status
  Parse raw string representation of ServiceState object
  Cross compile iperf3 into our measurement app.
nrAvailable | nrStatus | Inference
FALSE | NONE | Not in 5G service area
TRUE | NOT_RESTRICTED | In 5G service area, not connected to 5G
TRUE | CONNECTED | In 5G service area, connected to 5G
Notes: Due to these limitations, we developed our own tool from scratch [click] that logged information such as UE’s fine grained location, tower ID, signal strength information and so on.
[click]
To understand whether device is connected to 5G or not took some digging. From our initial experiments, we found that the Android’s ServiceState object [click] when converted to its raw string representation contained fields such as nrAvailable and nrStatus. Upon parsing followed by several field experiments and correlating with known ground truth information, we were able to infer the 5G status of the phone with high confidence.
[click]
Additionally, we also cross compiled iperf3 (a popular network performance measurement tool) into our measurement app.

## Slide 13: Challenge 3: Dealing with “Internet” Being the Bottleneck
Challenges (3/4)
Ultra-high bandwidth provided by 5G (esp. mmWave) can get affected when the Internet is congested.
Internet
LTE CORE
Content Server
Carrier Infrastructure
UE
Notes: Another challenge is related to Internet being the bottleneck.
[click] Due to the ultra-high bandwidth of 5G, the bottleneck of end-to-end path between the UE and the content-server may potentially shift from the carrier’s infrastructure to [click] the Internet. Since our goal is to focus on 5G carrier’s network performance, we do not want such a shift to happen. In other words, we do not want the Internet to be the bottleneck in our experiments.

## Slide 14: Challenge 3: Dealing with “Internet” Being the Bottleneck
Challenges (3/4)
This approach gave us the confidence of avoiding Internet being the bottleneck
UE (statistically) experiences high 5G throughput when downloading from this server
Upload speed of the server is high enough
Results comparable to state-of-the-art speed test services such as Ookla’s Speedtest app.
Select a content server such that -
Internet
LTE CORE
Content Server
Carrier Infrastructure
UE
Notes: We address this issue conducting several experiments and judiciously [click] select a content-server such that..
Downloading data from this server experiences high 5G throughput compared to other servers. [click]
The upload speed of the content server are way over the maximum achievable 5G throughput [click]
We ensure our results match with those generated by the state of the art speed testing platforms.
[click]
This approach gave us the confidence of avoiding Internet being the bottleneck
[next]

## Slide 15: Challenge 4: Non-Technical Challenges
5G coverage is spotty and hard to find
Travel to different cities and conduct on field experiments
Challenges (4/4)
Notes: And finally, we faced several non-technical challenges.
[click] Finding stable 5G coverage of different carriers were hard to find as the coverage was spotty.
[click] We also had to travel to multiple cities and conduct extensive on field experiments to evaluate multiple 5G carriers.

## Slide 16
Landscape Across 5G Carriers
Notes: We now present the findings from our measurement study. [click] starting with the landscape across 5G carriers.
[next]

## Slide 17: Landscape Across 5G Carriers – Throughput Performance
mmWave shows great potential upto 2 Gbps out in the wild!
mmWave have 2x-to-4x higher median throughput than mid-band
UE-Stationary
6 locations @ ATL
How Different Carriers Perform?
Setup:
Notes: Keeping the phone stationary, we examine the download speeds across different 5G carriers [click] using two servers in the US, one on the east coast and another on the west. This experiment was conducted in Atlanta.
We find that [click] commercial 5G exhibits great performance. For example, Verizon – a millimeter wave based 5G carrier - was able to achieve 2 Gbps downlink throughput over TCP – which is considerably better than today’s top-notch residential broadband networks.
Secondly, T-Mobile and Verizon, both which use millimeter wave technology [click] provide a much higher median throughput compared to Sprint’s mid-band 5G. This demonstrates the advantage of millimeter wave 5G and its ultra high speed.
[next]

## Slide 18
Landscape Across 5G Carriers
Impact of User Mobility
Notes: Next we take a look at the impact of mobility on different 5G carriers

## Slide 19: Impact of User Mobility
UE-Driving (20 to 50 km/hr)
Loop @ Atlanta
Mobility greatly affects mmWave performance
  Verizon and T-Mobile exhibit significant throughput fluctuation (often going to 0)
  T-Mobile handles handoffs more poorly than Verizon. e.g. TCP connections often got completely disconnected
In contrast, Sprint shows better ability to handle mobility than mmWave.
US East
Setup:
Notes: While driving in a car in Atlanta with speeds between 20 to 50 km/hour, we measure the download speed at the UE to understand the impact of mobility on 5G performance.
[click]
Verizon and T-Mobile both exhibit significant throughput fluctuation with the throughput often dropping close to 0 Mbps. This is due to frequent handoffs and blockages incurred by nearby buildings and vehicles.
[click]
We also found that T-Mobile handled handoffs more poorly than Verizon. On most occasions, mobility would completely disconnect TCP connections on T-Mobile.
[click]
Sprint on the other hand exhibits higher average throughput and lower throughput variation during most of the time. This shows Sprint has better ability to handle user mobility than millimeter wave signals due to the omni-directional nature of mid-band frequency.
[next]

## Slide 20
Landscape Across 5G Carriers
Impact of User Mobility
Handoffs in NSA 5G
Notes: Next, we try to understands handoffs in the present day non-standalone 5G
[next]

## Slide 21: Handoffs in NSA 5G
Tower
A
right
left
A
left
left
Tower/Panel
Active Radio Type
5G
A
right
5G
A
right
5G
B
4G
left
B
5G
A
4G
vertical
Tower
B
horizontal
vertical
5G to 5G
(same tower)
5G to 5G
(diff. tower)
vertical
vertical
Primitive
Combinational
Handoff
Type
Handoffs in 5G (1/2)
Alice
Notes: Consider Tower A is a 5G base station having two panels –
[click] one on the left side and
[click] another on the right.
[click]
Assume, Alice is connected to the left panel of tower A with 5G connectivity.
[click]
As she walks along the path, there is a handoff from the left-5G panel to the right-5G panel.
But since all the control signaling is happening over LTE, we observed such a 5G to 5G handoff associated with the same tower happens in two stages.
[click]
In the first stage, Alice experiences a handoff from 5G to 4G. Such a change in wireless technology is referred to as a vertical handoff.
[click]
in the second stage, another vertical handoff takes place but this time the radio type changes from 4G to 5G. Note, in this whole process, we were connected to the same tower A, but moved between panels.
[click]
The combination of the two primitive vertical handoffs resulted into a 5G to 5G handoff associated with the same tower.
In general, we define a combinational handoff as a type of handoff that corresponds to a high-level event that cannot be realized by a single primitive handoff type.
[click]
Now as Alice continues to walk towards another Tower, say B which again has two panels - left and right.
[click]
This time we see that she experienced a different type of combinational handoff – a 5G to 5G handoff involving two different towers A to B.
[click]
We observed this handoff event also consisted of two stages, the first one is when Alice having 5G connectivity moved from tower A to Tower B but with 4G active, resulting in a horizontal and vertical handoff occurring together as a single primitive handoff.
[click]
In the second stage, Alice -- who is now connected to tower B experiences a vertical handoff making her 5G connection active with tower B.
While these two scenarios illustrate two combinational handoffs, we observe that often times the primitive handoffs form more complex sequences and other 5G carriers also exhibit similar behavior. More details about handoffs observed in NSA 5G is explained in the paper.

## Slide 22: Handoff Analysis
UE experiences a total of 31 primitive handoffs (16 combinational) within 8 minutes!
Frequent handoffs causes frequent throughput fluctuations
Walking a 700m loop @ MPLS
mmWave
Handoffs in 5G (2/2)
US East
Setup:
Notes: Given the knowledge about the primitive and combinational handoffs in non-standalone 5G, we conduct an experiment with low mobility in Minneapolis area using Verizon’s 5G service. Holding the phone in our hand, we walk a loop of 700 meters spanning for roughly 8 minutes. While walking, we keep a downloading session active on the phone, and [click] log the perceived throughput and handoff activity events over time.
[click]
We find that the phone experiences a total of 31 primitive handoffs and bounces between 4G and 5G for 13 times.
While this may seem to be a side effect of non-standalone 5G, we still find a total of 16 combinational handoffs during this short walk. Such high number of handoffs especially while using millimeter wave is inevitable due to the small footprints of the 5G base stations.
[click]
Frequent handoffs results the throughput to highly fluctuate between 0 to 1Gbps.

## Slide 23
Landscape Across 5G Carriers
Impact of User Mobility
Handoffs in NSA 5G
Line of Sight Performance
mmWave
Notes: We now take a closer look at millimeter wave 5G’s performance by evaluating under clear line of sight conditions between the smartphone and the base station.

## Slide 24: Line of Sight - Throughput Performance
5G speeds up to 10x times better than LTE
5G exhibits higher throughput variations than LTE
Interestingly, 5G throughput improves as TCP concurrency level increases. We wonder why…
  carrier restrictions?
  backhaul unable to support?
(mmWave) Line of Sight Performance (1/2)
Setup:
UE-Stationary
mmWave
US East
Notes: In this experiment, we keep the UE stationary, [click] and vary the number of TCP connections used to download the content from the server. [click] We compare 5G’s throughput performance with that of existing LTE.
[click]
Results show that 5G speeds can improve upon LTE by a factor of 10 times! For instance, [click] With 8 TCP connections, the median LTE throughput is at about 167 Mbps while 5G is at 1.5Gbps
[click] 5G exhibits much higher variations due to the physical layer characteristics of millimeter wave as well as potential inefficiencies at other layers. For example, small form-factor of smartphones makes engineering a 5G modem and antenna system challenging.
[click] Its interesting to see that 5G throughput improves as the TCP concurrency level increases. Using 1 TCP connection, the throughput peaks at around 500 Mbps while the bandwidth is fully utilized when there are more than 8 concurrent connections.
We believe this could due to the following reasons
[click} - carrier imposing per-TCP-connection rate limiting
[click] - or that the backhaul infrastructure is unable to support very high throughput for single connection.
This will encourage application developers to aggressively increase the TCP concurrency that may adversely affect the TCP performance on other types of networks.
Next, we use the same setup [next] to also measure the

## Slide 25: Line of Sight - Round Trip Times
RTTs (and single-way latency) offered by 5G remains high
w/ payload: as TCP concurrency increases, RTT in 5G increases but is way better than LTE
with payload
Setup:
UE-Stationary
mmWave
US East
(Ping)
(mmWave) Line of Sight Performance (2/2)
Notes: round trip times and investigate the latency incurred using millimeter wave technology.
[click]
Using simple pings, we find that 5G and LTE exhibit similar round trip times. The first hop latency of 5G -- which presumably covers the RAN or radio access network -- also show no significant improvement over LTE.
[click]
With payload, we find that LTE round trip times inflate drastically because of its deep in-network buffers. But it is however less severe in 5G.
Nonetheless, the latency offered by today’s 5G remains high. We believe this to be due to two reasons.
First, Today’s 5G is NSA-based thus bound by LTE’s control plane mechanisms.
Second, lack of or limited use of edge support
Next, [next] we take a look at non-line of sight performance.

## Slide 26
Landscape Across 5G Carriers
Impact of User Mobility
Handoffs in NSA 5G
Line of Sight Performance
Non-Line of Sight Performance
X
mmWave
mmWave
Notes: [next] we take a look at non-line of sight performance.

## Slide 27: NLoS Performance (with Effective Multipath)
In outdoor environment with structures such as concrete buildings that can effectively reflect mmWave signals, we observe that 5G connection is able to persist even with sudden introduction of blockage between UE and tower with minor performance degradation.
(mmWave) Non-Line of Sight Performance (1/3)
Setup:
UE-Stationary
mmWave
US East
Alice
X
Bob
Notes: In outdoor urban setting, millimeter wave signals can reflect of surfaces that posses good reflection characteristics.
For instance, in downtown Minneapolis, our experiments show that introducing an obstruction in between the UE and 5G panel causes slight degradation in performance [click] which is most likely due to the time taken to recalibrate the highly directional millimeter wave beams for establishing a reflective non-line of sight path.
[next]

## Slide 28: NLoS Performance - Which Materials Obstruct and Which Don’t?
(mmWave) Non-Line of Sight Performance (2/3)
5G-NR
Panel
Notes: To get a better understanding on the penetration characteristics of millimeter wave signals, we next ask the question which materials obstruct millimeter waves and which don’t.
[click]
We used the setup as shown in this photograph of our hotel room in Chicago equipped with an awning window directly facing a [click] 5G panel located at a distance of 62 meters. Glass pane on the window was slightly tinted and coated with UV protection material. When the window was closed, our phone fell back to 4G suggesting millimeter waves are obstructed by tinted glass with UV filters. While the window was open, we place different types of materials to empirically understand the penetration characteristics of millimeter wave signals.
Note only when window is open, there is a clear line of sight to the 5G panel. Thus, such a setup eliminated any unwanted multipaths.
With this setup, [next]

## Slide 29: mmWave - Which Materials Obstruct and Which Don’t?
5G mmWave signals penetration/obstruction characteristics
obstructed by: tinted or UV-coated glass, human body, walls
pass through: clear glass, backpack, cardboard box
Setup:
UE-Stationary
mmWave
US East
(mmWave) Non-Line of Sight Performance (3/3)
Notes: we first consider [click]a human body as the obstruction followed by a hand.
In both cases, our phone fell back to 4G leading to significant drop in throughput.
[click]
We repeat the same experiment with other types of obstructions. We find that millimeter wave signals can pass through objects such as card boards, back packs and clear glass. However, they hardly penetrate human body and walls.

## Slide 30
Landscape Across 5G Carriers
Impact of User Mobility
Handoffs in NSA 5G
Line of Sight Performance
Non-Line of Sight Performance
Application Performance
X
mmWave
mmWave
mmWave
Notes: Finally we look at the impact of millimeter wave 5G on some real applications.
[next]

## Slide 31: Page Load Times & Download Performance Over the Web
5G minimizes web page load times (PLT) for heavy-websites with large amount of multimedia content.
UE-Stationary
mmWave
LoS to Tower
Chrome Browser App.
Setup:
UE-Stationary
mmWave
LoS to Tower
8-Parallel TCP Conn.
Setup:
Not surprisingly, CDNs perform far better than location-based VMs
Interestingly, all cloud servers exhibit low average throughput over HTTP(s) compared to iPerf throughput shown earlier – bound by worst performing TCP connection.
Workload: Download 1GiB file
Average
(mmWave) Application Performance
Notes: The web is a critical piece in the mobile ecosystem. We utilize [click] Chrome browser app. to load the [click] landing pages of several popular websites.
Based on the results we’ve seen so far in the presentation, it shouldn’t be surprising that [click] 5G does not bring much improvements over 4G on page load times except for heavy websites that contain many images and other multimedia content.
[click]
We also investigate the download performance over HTTPS by fetching a 1GiB file from several cloud and CDN providers. We developed a custom HTTPS downloader app. that established 8 TCP connections, each fetching 1/8th of the target file. [click] Figure at the bottom right shows the average throughput perceived by the 5G device for each of the different cloud / CDN provider.
[click] No doubt CDNs performed better than location-based virtual machines.
[click] However, iperf-based experiments on the very same virtual machines with 8 TCP connections fetched data at over ~1 Gbps throughput which much higher than 250 Mbps as observed over HTTPS.
One of the reason for such degraded performance over the web is that the total time taken to download the target file is bound by the worst performing TCP. In other words, if any of the 8 parallel TCP connections established with the server has poor throughput – the overall average throughput gets affected.
While this phenomenon exist in 4G as well, it gets amplified in 5G due to high-speed.

## Slide 32
Landscape Across 5G Carriers
Impact of User Mobility
Handoffs in NSA 5G
Line of Sight Performance
Non-Line of Sight Performance
Application Performance
X
mmWave
mmWave
mmWave
Concurrent Clients
Impact of
UE-Tower Distance
HTTP Protocols: HTTP1 vs HTTP2 vs HTTP3
UDP Performance
First-Hop
Latency
UE-Tower
Orientation
Impact of Weather
Notes: [click] We show results of many other experiments in our paper however in the interest of time, we skip them here.

## Slide 33: Key Takeaways from Today’s Commercial 5G
Commercial 5G still in its very infancy
mmWave 5G demonstrates impressive downlink throughput performance under LoS conditions + limited user mobility, and reasonable NLoS performance with reflective paths
5G across carriers do not yet achieve sub-millisecond latency
Frequent fluctuations in throughput performance caused due to handoffs and PHY-layer characteristics
High throughput variation coupled with current transport-layer mechanisms may confuse application logic
mmWave 5G’s performance severely affected by user mobility and obstructions
* Today’s 5G can benefit certain very specific use cases of a very niche segment of applications requiring “enhanced broadband”.
Enhanced
Broadband
Massive
Connectivity
Mission Critical
Communications
5G Band | … | Low-band | Mid-Band | mmWave
Frequency | … | 600 MHz | 850 MHz | 39 GHz
Launch | … | December 2019 | December 2019 | March 2020
October 2019
yet rapidly evolving
Standalone 5G/5GC
Multi-access Edge Computing (MEC)
*
Notes: Lets summarize the key takeaways from Today’s 5G Performance
[click]
With a download speed of 2Gbps, millimeter wave 5G has demonstrated impressive speeds. This is only achievable with clear line of sight and limited user mobility. Under non-line of sight conditions though, it is also worth mentioning that in environments with good signal reflection characteristics, carriers are able to achieve reasonable performance by quickly recalibrating the signals off reflective surfaces.
[click]
The biggest nightmare factors for millimeter wave signals are obstructions and user mobility. This is precisely the reason why 5G’s wide spectrum range includes mid-band and low-band frequencies to fill in such gaps. However, current commercial 5G deployments do not yet support multimode (or multiband) 5G.
[click]
There is no drastic latency improvement offered by 5G over 4G. This can be attributed to the non-standalone 5G deployment strategy currently in practice commercially and the lack of edge support. Thus none of the carriers are able to provide sub millisecond latency as promised by 5G.
[click]
Due to the frequent handoffs and physical layer characteristics of millimeter wave signals, we observed frequent fluctuations in throughput over time.
[click]
High throughput variation coupled with current transport layer mechanisms such as congestion control algorithms may confuse application layer logic such as video bitrate adaptation algorithms. These experiences highlight the need for cross layer efforts that are vital to improve 5G performance.
[click]
Looking back at the use cases promised by 5G, we find that today’s commercial 5G can only support a [click] very niche segment of applications requiring enhanced broadband capacity and that too under very specific scenarios such as having clear line of sight to 5G base station under limited to no user mobility.
While 5G’s standardization process and requirements have come a long way, [click] 5G is still in its very infancy in terms of commercially deploying and fulfilling its requirements. Additionally, [click] lack of Standalone 5G makes it difficult to exploit’s 5G core’s architectural features such as multi-access edge resources (or MECs), network slicing, and so on.
[click]
None the less, commercial 5G is rapidly evolving.
[click]
Since October 2019 – the time when this paper was submitted for review, we have seen T-Mobile has added low-band frequency to its 5G network, while AT&T has also made its mid-band as well as millimeter wave 5G services available to consumers.

## Slide 34: On-Going and Future Work
Modeling 5G Performance
Re-Visiting Transport Layer Mechanisms
Building 5G-Aware Applications
Notes: As part of our on-going and future work, we find that unlike in 4G or3G where location can be used for performance estimation, this is not true for 5G networks.. Several contextual and environmental factors such as the type of 5G service, location, time of the day, mobility level, device orientation, and several other dynamic factors need to be accounted for modeling 5G performance.
We also illustrate the need for cross layer mechanisms to make the applications as well as the transport layer address new challenges posed by 5G networks.
[click]

## Slide 35: Contributions | 5Gophers Platform – Open for Collaboration
Data collected from this paper is publicly available on our website
https://fivegophers.umn.edu/www20
Developed practical and sound measurement methodologies and conducted a first comprehensive study of 5G performance on COTS smartphones.
This dataset should serve as a “baseline” for studying the evolution of 5G performance.
Thank you !
To Collaborate
5Gophers
A platform to track 5G and conduct real 5G measurements in the wild
visit us @ https://fivegophers.umn.edu fivegophers@umn.edu
Notes: To conclude,
[click]
We conduct a first measurement study of commercial 5G over smartphones by developing our own measurement platform and methodologies.
[click]
The data collected from our study is available on our website.
[click]
Since these measurements were conducted when 5G just made its debut, our results should serve as an important baseline for evaluating 5G’s evolution.
Last but not the least, we have developed a platform called 5Gophers. This platform consists of mobile applications and tools required to conduct 5G measurements in the wild.
The 5Gophers public facing website also provides geographic visualizations of 5G coverage and performance maps of select cities in the US. We invite collaborators to be part of this platform.
[click]