## Slide 1: Adaptive Resilient Routing via Preorders in SDN
Eman Ramadan, Hesham Mekky, Braulio Dumba and Zhi-Li Zhang
University of Minnesota

## Slide 2: Agenda
Introduction
Limitations of Path-based Routing
Routing via Preorders
Realization in SDN
Conclusion

## Slide 3: Introduction
Adding more switches and links to networks
  Increases available parallelism
  An effective way to meet insatiable application demands for bandwidth
  Leads to a far richer network topology (often many diverse paths between two end points)
However, with the growing network scale
  The probability of failures becomes higher
  Resilient routing – e.g., via pro-active fast failover mechanisms – is imperative, to meet ever stringent availability, reliability and QoS requirements demanded by applications

## Slide 4: Path-based Routing Doesn’t Work!
Existing routing schemes for communication & SCADA control networks are path-based!
  compute one path (e.g., shortest) or multiple paths from s to d
  route traffic along the path or paths, e.g., via IP or MPLS protocol
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 5: Path-based Routing Doesn’t Work!
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Toy Network Example
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
O(2L) many (shortest) paths of length 2L!

## Slide 6: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 7: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 8: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 9: Path-based Routing Doesn’t Work!
Toy Network Example: fairly robust topology
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 10: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 11: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 12: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 13: Path-based Routing Doesn’t Work!
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 14: Beyond Path: Can We Do Better?
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
What about using a Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L

## Slide 15: Beyond Path: Can We Do Better?
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
What about using a Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Can survive arbitrary link/node failures as long as they do not disconnect s and d!

## Slide 16: Routing DAGs Sufficient for Resiliency?
Routing DAG (directed acyclic graph)
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically
Sufficient to guarantee optimal resiliency for any topology? i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?
New (slightly modified) Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L

## Slide 17: Routing DAGs Sufficient for Resiliency?
Routing DAG (directed acyclic graph)
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically
Sufficient to guarantee optimal resiliency for any topology? i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?
New (slightly modified) Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L

## Slide 18: Routing DAGs Sufficient for Resiliency?
Routing DAG (directed acyclic graph)
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically
Sufficient to guarantee optimal resiliency for any topology? i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?
New (slightly modified) Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L

## Slide 19: Routing DAGs Sufficient for Resiliency?
Routing DAG (directed acyclic graph)
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically
Sufficient to guarantee optimal resiliency for any topology? i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?
New (slightly modified) Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L

## Slide 20: Routing DAGs Sufficient for Resiliency?
Routing DAG (directed acyclic graph)
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically
Sufficient to guarantee optimal resiliency for any topology? i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?
New (slightly modified) Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
?

## Slide 21: Routing DAGs Sufficient for Resiliency?
Routing DAG (directed acyclic graph)
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically
Sufficient to guarantee optimal resiliency for any topology? i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?
New (slightly modified) Toy Network Example
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L

## Slide 22: Routing via PreOrders

## Slide 23: Routing via Preorders
Routing Preorder
  Mathematically, a preorder on a node set is a binary relation that is reflective and transitive, for any d, a path between s, d via u
Routing Preorder Graph (PrOG)
  Directed graph associated with a routing preorder
A
G
B
C
F
E
D
H
I
s = J
d = O

## Slide 24: Routing via Preorder & PrOG
Routing Preorder
Routing Preorder Graph (PrOG)
Traffic forwarding
  Split proportionally across outgoing links
  Bi-directed links generally not used under normal operations; invoked (along one direction) under failures
d = G
E
F
C
D
B
s = A

## Slide 25: Routing via Preorder: Failure Handling
Failure Handling Process:
  Upon failures, use alternative outgoing links if exist
d = G
E
F
C
D
B
s = A

## Slide 26: Routing via Preorder: Failure Handling
Failure Handling Process:
  Upon failures, use alternative outgoing links if exist
  If a node becomes a “sink”, de-activate incoming links
d = G
E
F
C
D
B
s = A
No Need for Global Topology
Information Exchange &
Route Recomputation

## Slide 27: Routing via Preorder: Recovery Process
Recovery Process:
  If a node/link recovers, re-activate outgoing links
d = G
E
F
C
D
B
s = A
Guarantee to Restore to the Original
Routing State

## Slide 28: Optimal Resilient PrOG Construction with Latency Constraints
d = G
E
F
C
D
B
s = A
Primary PrOG
d = G
E
F
C
D
B
s = A
H
I
J
K
Backup PrOG
Questions: do such PrOGS exist?
If yes, can they be constructed in polynomial time?

## Slide 29: -Complete Preorder Graphs (PrOGs)
B

## Slide 30: Realization in SDN

## Slide 31: Realization in Emerging Software-Defined Networks (SDNs)
The controller computes the routing preorder (satisfying latency constraints), then installs the corresponding rules in the relevant switches
Each switch forwards packets using the match-action data plane abstraction
Small functionality added to switches to maintain and update some internal states, and generate activation and deactivation tags
Switches perform some actions to handle link activation, deactivation and failure

## Slide 32: Resilient Routing via Preorders: Packet Forwarding
Each switch/router maintains a set of routing rules and states
Each packet carries two header fields
Eligible outgoing links at node u for forwarding packet to d:
Upon failure, update both header fields before rerouting

## Slide 33: Simple Demonstration & Evaluation
Routing via preorder implemented in Mininet with slightly modified Open vSwitch (OVS) using v.2.4
Simple Demonstration:

## Slide 34: Realization in SDN: Rule Examples
Match-action rules for switch D

## Slide 35: Simple Demonstration & Evaluation
Simple Demonstration:
a UDP traffic generator at host h1, attached to node A, sends datagrams to host h2, attached to node G
Traffic lasts for 20 seconds, sending around 90 pks/sec

## Slide 36: Simple Demonstration & Evaluation
Simple Demonstration:
a UDP traffic generator at host h1, attached to node A, sends datagrams to host h2, attached to node G
Traffic lasts for 20 seconds, sending around 90 pks/sec

## Slide 37: Simple Demonstration & Evaluation
Simple Demonstration:
a UDP traffic generator at host h1, attached to node A, sends datagrams to host h2, attached to node G
Traffic lasts for 20 seconds, sending around 90 pks/sec

## Slide 38: Simple Demonstration & Evaluation
Simple Demonstration:
a UDP traffic generator at host h1, attached to node A, sends datagrams to host h2, attached to node G
Traffic lasts for 20 seconds, sending around 90 pks/sec

## Slide 39: Simple Demonstration & Evaluation
Simple Demonstration:
a UDP traffic generator at host h1, attached to node A, sends datagrams to host h2, attached to node G
Traffic lasts for 20 seconds, sending around 90 pks/sec

## Slide 40: Simple Demonstration & Evaluation
link up
Simple Demonstration:
a UDP traffic generator at host h1, attached to node A, sends datagrams to host h2, attached to node G
Traffic lasts for 20 seconds, sending around 90 pks/sec

## Slide 41: Conclusion
Proposed a new routing paradigm – routing via preorders
  Circumvents the limitations of conventional path-based routing schemes
  Effectively takes advantage of topological diversity inherent in a network with rich topology for adaptive resilient routing
  Meets the QoS requirements (e.g., latency) of applications or flows
  Resilient against arbitrary k link or node failures (if network not partitioned)
Realized routing via preorders in SDN networks using the “match-action” data plane abstraction, with a preliminary implementation of it in Mininet

## Slide 42: Thank you