## Slide 1: Taproot: Resilient Diversity Routing with Bounded Latency
Eman Ramadan, Hesham Mekky, Cheng Jin,
Braulio Dumba, Zhi-Li Zhang
Please don’t forget to install the fonts
provided besides this presentation.
After installing the fonts, please re-open this presentation.

## Slide 2: Network Scale, Failure, and Resilient Routing
Adding more switches and links to networks
  Increases available parallelism
  An effective way to meet insatiable application demands for bandwidth
  Leads to a far richer network topology (often many diverse paths between two end points)
However, with the growing network scale
  The probability of failures becomes higher
  Resilient routing – e.g., via pro-active fast failover mechanisms – is imperative, to meet ever stringent availability, reliability and QoS requirements demanded by applications

## Slide 3: Path-based Routing Inadequate
Existing routing schemes for communication & SCADA control networks are path-based!
  compute one path (e.g., shortest) or multiple paths from s to d
  route traffic along the path or paths, e.g., via IP or MPLS protocol
Fundamental Limitations of Conventional Path-based Routing:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 4: Path-based Routing Inadequate
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Toy Network Example
O(2L) many (shortest) paths of length 2L!
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!

## Slide 5: Path-based Routing Inadequate
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
A single shortest path can’t survive a single link failure!
Toy Network Example

## Slide 6: Path-based Routing Inadequate
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
What about using two paths; One primary and one backup?
Many two-link failure events (one on each path) render both paths invalid, even if s & d are still connected!
Toy Network Example

## Slide 7: Path-based Routing Inadequate
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
What about using two path; One primary and one backup?
Many two-link failure events (one on each path) render both paths invalid, even if s & d are still connected!
Toy Network Example

## Slide 8: Path-based Routing Inadequate
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
No single link failure disconnects s & d
Only 3 types of two-link failure events partition the network!
Type 1
fairly robust topology
Toy Network Example

## Slide 9: Path-based Routing Inadequate
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
No single link failure disconnects s & d
Only 3 types of two-link failure events partition the network!
Type 2
Toy Network Example

## Slide 10: Path-based Routing Inadequate
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
No single link failure disconnects s & d
Only 3 types of two-link failure events partition the network!
Type 3
Toy Network Example

## Slide 11: Path-based Routing Inadequate
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Beside these 3 types, under any other two-link failure events, there always exists a path from s to d !
Toy Network Example

## Slide 12: Path-based Routing Inadequate
Path-based Routing Can’t Ensure Resiliency against Arbitrary Two-Link Failures:
  paths are rigid: must be precisely specified a seq. of nodes & links
  paths are fragile: failure of any node or link renders it invalid!
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
In fact, many (random) 3 or more link failure events do not disconnect s & d, or partition the network!
Unless we enumerate all paths, no path-based routing scheme would guarantee connectivity from s to d when a path exists!
Toy Network Example

## Slide 13: Beyond Path: Can We Do Better?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
What about using a Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Toy Network Example

## Slide 14: Beyond Path: Can We Do Better?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
Can survive arbitrary link/node failures as long as they do not disconnect s and d !
What about using a Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Toy Network Example

## Slide 15: Routing DAGs Sufficient for Resiliency?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
New (slightly modified) Toy Network Example
Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Is DAG sufficient to guarantee optimal resiliency for any topology?
i.e., ensure data delivery from s to d under arbitrary failures as long as they do not disconnect the two nodes?

## Slide 16: Routing DAGs Sufficient for Resiliency?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
New (slightly modified) Toy Network Example
Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Is DAG sufficient to guarantee optimal resiliency for any topology?

## Slide 17: Routing DAGs Sufficient for Resiliency?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
New (slightly modified) Toy Network Example
Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Is DAG sufficient to guarantee optimal resiliency for any topology?

## Slide 18: Routing DAGs Sufficient for Resiliency?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
New (slightly modified) Toy Network Example
Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Is DAG sufficient to guarantee optimal resiliency for any topology?

## Slide 19: Routing DAGs Sufficient for Resiliency?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
?
New (slightly modified) Toy Network Example
Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Is DAG sufficient to guarantee optimal resiliency for any topology?

## Slide 20: Routing DAGs Sufficient for Resiliency?
v4
v8
v12
v2
s=v1
v5
v6
v3
v7
d=v2L+1
v10
…
v4L-2
v4L
New (slightly modified) Toy Network Example
Routing DAG (directed acyclic graph)?
  no need to pre-specify any specific path
  any outgoing link in the routing DAG can be dynamically utilized
Is DAG sufficient to guarantee optimal resiliency for any topology?

## Slide 21: Outline
Routing Via Preorders
Handling Failure & Recovery
Realization in SDN
Demonstrate Taproot’s superiority over existing approaches

## Slide 22: Routing via Preorders
Routing Preorder
  Mathematically, a preorder on a node set is a binary relation that is reflective and transitive, for any d, a path between s, d via u
Routing Preorder Graph (PrOG)
  Directed graph associated with a routing preorder
src
dst
a) Weighted Topology
b) Latency-Complete PrOG

## Slide 23: Routing via Preorder & PrOG
Routing Preorder
Routing Preorder Graph (PrOG)
Traffic forwarding
  Split proportionally across outgoing links
  Bi-directed links generally not used under normal operations; invoked (along one direction) under failures
src
dst
Notes:   A flow is mapped to these PrOGs without pre-specifying any path; packets can dynamically traverse any (directed) path

## Slide 24: Resilient PrOG Construction with Latency Constraints
Given a flow F from s to d with latency constraints:
  Under normal operation, latency requirement 𝜏F
  Under failures, latency requirement F ≥ 𝜏F
Problem: find a latency-complete PrOG which:
  Meets the latency requirements under both conditions
  Resilient against failures
Resilient Diversity Routing with Bounded Latency: Under arbitrary failure scenarios, as long as there is a path from s to d with latency ≤ 𝜏, data delivery of flow F from s to d is guaranteed!
Do such PrOGs exist? If yes, can they be constructed in polynomial time?

## Slide 25: Latency-Complete Preorder Graphs (PrOGs)
Given a graph G = (V, E), source s, destination d, and latency 𝜏 which can be equal to either 𝜏min (𝜏max) latency of shortest (longest) simple path from s to d
Latency-Complete PrOG with respect to any 𝜏 > 0 is an oriented subgraph which contains any path P from s to d with ɸ(P) ≤ 𝜏.
Latency-Complete PrOG can be computed in O(n2) for each destination. Using a modified two-phase BFS process:
  Start breadth first search from the dst d. At each step for each node v, record its min latency to d, and those of its neighbors;
  Start with the src s, retrace the steps, and prune any branch whose latency exceeds 𝜏
Please refer to the paper for more details and proof of correctness

## Slide 26: Outline
Routing Via Preorders
Handling Failure & Recovery
Realization in SDN
Demonstrate Taproot’s superiority over existing approaches

## Slide 27: Routing via Preorder: Failure Handling
Failure Handling Process:
  Upon failures, use alternative outgoing links if exist
  If a node becomes a “sink”, de-activate incoming links
src
dst
No Need for Global Topology Information Exchange & Route Recomputation

## Slide 28: Routing via Preorder: Recovery Process
Recovery Process:
  If a node/link recovers, re-activate outgoing links
src
dst
Guaranteed to Restore the Original Routing State

## Slide 29: Resilient Routing via Preorders: Packet Forwarding
Each switch/router maintains a set of routing rules and states:
  Routing rules for the outgoing links from the latency-Complete PrOG (prioritized acc. to latency)
  𝜏d(u): min. latency to dst d from node u
  𝜏d(u → v): min latency to dst d via link u → v
Each packet carries two header fields initialized as following:
Packet Forwarding:
  Node u determines nexthop v is eligible or not to forward packets to d iff 𝜏d(u → v) ≤ 𝜏
  Then, u updates latency field: 𝜏 := 𝜏 - ɸuv before forwarding it to v
Upon failure:
  Both header fields are updated before rerouting as following:
Latency field 𝜏 := 𝜏F
Latency field 𝜏 := 𝜏 + Δ𝜏
Latency offset field Δ𝜏 := F - 𝜏F
Latency offset field Δ𝜏 := 0

## Slide 30: Outline
Routing Via Preorders
Handling Failure & Recovery
Realization in SDN
Demonstrate Taproot’s superiority over existing approaches

## Slide 31: Realization in Emerging Software-Defined Networks (SDNs)
The controller computes the routing preorder (satisfying latency constraints), then installs the corresponding rules in the relevant switches
Each switch forwards packets using the match-action data plane abstraction
Small functionality added to switches to maintain and update some internal states, and generate activation and deactivation tags
Switches perform some actions to handle link activation, deactivation and failure

## Slide 32: Realization in SDN: Rule Examples
Match-action rules for switch F
Routing via preorder implemented in Mininet with slightly modified Open vSwitch (OVS)

## Slide 33: Outline
Routing Via Preorders
Handling Failure & Recovery
Realization in SDN
Demonstrate Taproot’s superiority over existing approaches

## Slide 34: Exploring Topological Diversity
Primary Path: shortest-path between the src and dst
Backup Path: a disjoint path after removing the primary path between src & dst
Backup Links: a backup path is created for each link on the primary path
Latency-Complete PrOGs: we use multiple PrOGs with 𝜏 = d, d+1, d+2 where d is the shortest-distance between src & dst
Topology | Nodes | Edges | Max Degree | Average Degree
AS1221 | 83 | 131 | 14 | 3.16
AS3967 | 91 | 180 | 10 | 3.96
AS1755 | 111 | 234 | 11 | 4.22
AS3257 | 151 | 288 | 30 | 3.81

## Slide 35: Percentage of Disconnected Pairs
Key Observations
PrOGs with 𝜏 = d+2 reduce the number of disconnected src-dst pairs.
Taproot utilizes network diversity, while satisfying latency constraints without path enumeration.
Unlike backup link protection technique, Taproot has performance guarantee.

## Slide 36: PrOG Overhead
Still within the limits of current TCAMs

## Slide 37: Performance Evaluation
We use Google’s WAN topology[1]
We compare the performance of Taproot with DDC[2], which employs link reversals to reconstruct a new DAG when a node becomes sink.
A UDP traffic generator is used to send around 50K packets from h1 (attached to s1) to h2 (attached to s12), we use 𝜏F = 5, F = 9.
[1] Sushant Jain, Alok Kumar, Subhasree Mandal, et al. B4: Experience with a globally-deployed software defined WAN. ACM SIGCOMM Computer Communication Review 43, 4 (2013), 3–14. [2] Junda Liu, Aurojit Panda, Ankit Singla, Brighten Godfrey, Michael Schapira, and Scott Shenker. Ensuring Connectivity via Data Plane Mechanisms. In NSDI 2013.

## Slide 38: Performance Evaluation
Key Observations
Convergence time increases with the number of link failures.
In DDC, packets experience longer latency till the convergence process is done.
In Taproot, the latency is always less than F = 9, regardless of the number of link failures.

## Slide 39: Conclusion
Realized routing via preorders in SDN networks using the “match-action” data plane abstraction
Proposed a new routing paradigm – routing via preorders
  Circumvents the limitations of conventional path-based routing schemes
  Effectively takes advantage of topological diversity inherent in a network with rich topology for adaptive resilient routing
  Meets the QoS requirements (e.g., latency) of applications or flows
  Resilient against k link or node failures (if network not partitioned)