## Slide 1: When Raft Meets SDN: How to Elect a Leader and Reach Consensus in an Unruly Network
Yang Zhang, Eman Ramadan, Hesham Mekky, Zhi-Li Zhang
University of Minnesota

## Slide 2: Introduction
Consensus Algorithm

## Slide 3: Introduction
Consensus algorithm is essential for SDN distributed control plane
Consensus Algorithm
Software Defined Network
Application Layer
Control Plane
Data Plane
Applications
Network Operating Systems
Network Device
Network Device
Network Device
Network Device
API
API
API
Control to Data Plane Interface

## Slide 4: Problems in SDN Distributed Control Plane
SDN control plane setup
Cyclic dependencies
control network connectivity
consensus algorithm
control logic managing the network
In consensus algorithm
server failure has been studied for decades
full mesh connectivity is assumed
what if network fails?
new failure scenarios arise in SDN

## Slide 5: RAFT: a representative consensus algorithm
At any given time, each server is either:
  – Leader: handles all client interactions, log replication, etc.
  – Follower: completely passive
  – Candidate: used to elect a new leader
• Normal operation: 1 leader, N-1 followers
Follower
Candidate
Leader

## Slide 6: RAFT Leader Election
Follower
Candidate
Leader
times out,
start election
receives votes
from majority
times out,
new election
discovers server with higher term
discovers current leader or a higher term
start
*Term is defined as virtual time period in Raft
Vote criteria: 1) highest term, 2) latest log

## Slide 7: RAFT MEETS SDN
Control Cluster under Normal Operations.
R2
R3
R4
R5
R1

## Slide 8: RAFT MEETS SDN
R1
R3
Control Cluster under Normal Operations.
Oscillating Leadership.
Condition. Up-to-date servers have a quorum, but they cannot communicate with each other.
R3
R1
R3
R1
R3
R1
R4
R5
R2
R2
R3
R4
R5
R1

## Slide 9: RAFT MEETS SDN
No Leader Exists.
Condition. Some servers have a quorum, but they have obsolete logs, and servers having up-to-date logs, do not have a quorum.
R5
R4
R3
R2
R1
R1

## Slide 10: POSSIBLE SOLUTIONS
Solution Expectation
  all-to-all connectivity among cluster members as long as the network is not partitioned.
Gossiping (overlay network)
  Pros: easy to implement
  Cons: no guarantee to work in all scenarios; heavy overhead
Routing via Preorders
  Pros: built-in resiliency in control plane; no modification to consensus algorithm
  Cons: requires path calculation ahead of time

## Slide 11: Routing via Preorder: Failure Handling
Failure Handling Process:
  Upon failures, use alternative outgoing links if exist
  Group table is used for implementing all possible alternative paths
d = G
E
F
C
D
B
s = A
It guarantees a network where two nodes are always reachable as long as there is no partition.
proved

## Slide 12: PRELIMINARY RESULTS
Experiment Setup
Raft Implementation: Raft C++ implementation in LogCabin
Six Docker containers: 5 servers and 1 client
Five Software switches: Open vSwitch
Simulating the two failure scenarios:
  Oscillating Leadership
  No Existing Leader

## Slide 13: PRELIMINARY RESULTS
Raft: leadership keeps oscillating among servers (unstable).
Raft: no viable leader (liveness lost).
PrOG: leadership is stable.
Vanilla Raft is not stable under failure scenarios, while PrOG-assisted Raft is stable.

## Slide 14: PRELIMINARY RESULTS
Latency of a request operation increases under failure scenarios
Client suffers much more failed attempts for accessing cluster leader in vanilla Raft.

## Slide 15: Summary
SDN controller liveness depends on all-to-all message delivery between cluster servers
Raft is used to illustrate the problem induced by interdependency in the design of SDN distributed control plane
Possible solutions are discussed to circumvent interdependency issues.
Preliminary results show the effectiveness of PrOG in improving the availability of leadership in Raft used by critical applications like ONOS.